## Slide 1
UNIMORE · REAL-TIME EMBEDDED SYSTEMS · A.Y. 2025/2026
DON'T PANIC
Bloated MP3 Player — Deadline Analysis
From 9 concurrent peripherals on ESP32-S3 to provable scheduling guarantees. Rate-Monotonic · EDF · PIP / PCP · Processor Demand Criterion
Henry Letellier • ESP32-S3 WROOM (dual-core 240 MHz) • FreeRTOS via Arduino
7 slides • No firmware modified • Analysis from bonus/rta/*.py
bonus/rta/lenv • python-pptx + matplotlib • 2026-09-01
WHAT THIS DECK PROVES
U & Bound
U=0.947 > 0.757 → RTA needed
RTA
b,c,d OK · a R=41 > 40 fails RM
EDF
U=0.617 ≤ 1 and PDC passes (600 pts)
Blocking
PCP halves B vs PIP (10→4, 10→6)
Complexity
Busy period L*=10: 600→1 point (600×)
The Hitchhiker's answer was 42. Our answer is 40: the period where RM breaks.
Tip: wave at the HC-SR04 to pause. Wave twice to bail out — just like deadline handling.
01 / 07

## Slide 2
01 — SYSTEM
Bloated by design, real-time by necessity
ESP32-S3 dual-core · FreeRTOS · 9 tasks · “17 sensors on one I²C bus”
HARDWARE — THE BOM OF DOOMED PERIPHERALS
Display
GMG12864-06D 128×64 SPI (ST7565R) CS10 RST9 DC8
Char LCDs
2004A (0x27) folder/track + 1602A (0x26) Vogon poetry — I²C SDA2/SCL1
Audio
2× MAX98357A I²S BCLK16 WS47 DIN17/18 — Helix MP3 + PSRAM
Sensors
AHT20+BMP280 (env) · MPU-9250 (IMU) · HC-SR04 (TRIG14 ECHO13)
Input / Light
EC11 rotary A42 B15 SW12 · WS2812B 16×16 matrix pin 41
Storage
microSD SDMMC 1-bit CLK39 CMD38 D0 40
Compute
Freenove ESP32-S3 WROOM dual-core 240 MHz · Arduino + FreeRTOS
FREERTOS MAPPING — CORE & STACK REALITY
Task
Prio
Core
Stack
Note
Audio
3
0
16 384
Helix + FATFS deep chain
Input
2
0
16 384
SD open() overflow fix
UI / LED / Matrix
1
1
4–8K
33 ms UI, I²C traffic
Sensor / Serial / Vogon
1
0/1
4–8K
I²C 50 ms timeout, BLE GATTS
Lesson: Audio on core 0 prio 3 isolates decode; everything else 1 — dual-core = interference domain partition.
WHY THIS NEEDS ANALYSIS — CONCURRENCY REALITY
The joke: 17 peripherals arguing on one I²C bus.
• FreeRTOS preemptive scheduler ticks every 1 ms — 9 tasks compete, priorities decide who preempts whom.
• Shared buses: I²C (AHT20/BMP280 + 2 char LCDs), SPI (LCD + font ROM), SDMMC (FATFS). All need bounded blocking.
• Stacks matter: printf(%a.1f) pulls _dtoa_r + malloc; Audio/Input blew 8K → 16K canary. Not in the model, but real.
• Audio cannot starve: double-buffered I²S with Helix fixed-point decode; Input (SD open) runs near-Audio depth — hence prio 2.
• Question for this deck: if we idealise 4 tasks, can RM guarantee deadlines? If not, does EDF? At what cost?
Takeaway: model 4 periodic tasks (b,c,d,a) to stress the method, then map back to the 9-task dual-core reality → slide 7.
02 / 07

## Slide 3
02 — TASK MODEL
From 9 threads to 4 canonical tasks
Enough to prove the point, small enough to compute by hand — then verify with bonus/rta
TASK SET — RM ORDER (shortest period = highest priority)
Task
C (WCET)
T = D
Prio (RM)
U = C/T
τ_b
2
8
1
0.250
τ_c
3
10
2
0.300
τ_d
4
18
3
0.222
τ_a
7
40
4
0.175
Total utilisation U = Σ C/T
0.947
D = T for all tasks (implicit deadlines). Solver: bonus/rta/rta_solver.py
UTILISATION BOUND — SUFFICIENT, NOT NECESSARY
Liu & Layland (1973) — U ≤ n(2¹/ⁿ − 1)
n = 4
Bound = 4·(2¹/⁴ − 1)
= 0.757
Actual U = 0.947
U > Bound (0.947 > 0.757)
INCONCLUSIVE → RTA
Bound is pessimistic: harmonic periods pass more often. RTA (next slide) is exact — iterate R = C + Σ ceil(R/Tₕ)·Cₕ until fixed point or deadline miss.
WHAT RTA ACTUALLY COMPUTES — exact response-time iteration
R_i⁰ = C_i R_iᵏ⁺¹ = C_i + Σ_{h∈hp(i)} ceil(R_iᵏ / Tₕ) · Cₕ
Stop when Rᵏ⁺¹ = Rᵏ (schedulable if ≤ D) or R > D (miss). Each iteration adds interference from all higher-priority jobs that fit in the window.
INTUITION: “How long am I delayed by everyone above me?”
• hp(i): higher-priority tasks • ceil(R/Tₕ): how many jobs of h interfere • Converges in ≤ D steps → pseudo-polynomial
03 / 07

## Slide 4
03 — RESPONSE-TIME ANALYSIS
RM: three pass, one fails at 41 > 40
bonus/rta/rta_solver.py • y is baseline (U8g2) but here y is time
RTA ITERATION — FIXED-POINT TRACES
Task
Iter
R
≤ T?
τ_b
1: 2
2
✓ 2 ≤ 8
τ_c
2: 5 → 5
5
✓ 5 ≤ 10
τ_d
3: 4→9→14
14
✓ 14 ≤ 18
τ_a
4: 7→14→27→34→41
41
✗ 41 > 40
τ_d example: R⁰=4 → R¹=4+ceil(4/8)·2+ceil(4/10)·3=9 → R²=4+ceil(9/8)·2+ceil(9/10)·3=14 stable.
τ_a: 7→14→27→34→41 crosses D=40 on iteration 4 — RM cannot schedule the full set. σ = interferences from b,c,d stacking.
Exact, not just sufficient. This is why the bloated player isolates Audio (prio 3, core 0).
GANTT — PREEMPTIVE RM OVER [0,40) (bonus/rta/schedule_sim.py → RMSim)
C switches
18
Slots
19
Idle
0.7%
Worst slack
τ_d: 4 / 18
Read: a only runs 14–16, 27–30, 35–36 — always preempted. Visual proof of R_i starvation.
SO WHAT FOR THE PLAYER?
RM is optimal among fixed priorities, but this set defeats it. Options:
• Drop U (faster CPU, lighter WCET, longer periods) — not possible on ESP32-S3 at 240 MHz with Helix.
• Switch to EDF (dynamic) — next slide. • Partition cores: we already do (Audio core 0, UI core 1) — formal equivalent of reducing n per core.
“The Guide says: don’t panic. The analysis says: τ_a misses by 1. That’s as real as it gets.”
04 / 07

## Slide 5
04 — ALTERNATIVES
RM vs EDF (preemptive) vs EDF (non-preemptive)
Same tasks, same window [0,40) — only the rule changes
GANTTS — VISUAL COMPARISON (all to same scale)
↑ RM: fixed, period-rate — a starves
↑ EDF preemptive: deadline-driven — a finishes at 32 (meets D=40!)
↑ EDF non-preemptive: no preemption — a runs 14–21 (blocking) but no interleaving
NUMBERS — AT A GLANCE
Scheduler
CS
Meets?
Notes
RM pre.
18
✗ a fails
optimal FP
EDF pre.
16
✓ all meet
dynamic, optimal*
EDF non-pre.
12
✓ but frag.
blocking ↑
EDF optimality*: on uniprocessor with D≤T, if any schedule meets all deadlines, EDF does. Here RM fails, EDF succeeds.
Non-preemptive reduces switches (12 vs 16) but inflates blocking — a must wait for b/c/d to finish (14–21). FreeRTOS is preemptive for a reason.
Player tie: Audio is soft-real-time (glitch = audible). Input/UI are firm. Preemptive EDF intuition justifies Audio prio 3 — it must preempt.
BOTTOM LINE
Fixed priority loses here; dynamic wins. Next: what if tasks share resources? RM/EDF optimality evaporates without a blocking protocol.
05 / 07

## Slide 6
05 — SHARED RESOURCES
R1–R5: PIP vs PCP blocking (bonus/rta/blocking_times.py)
One lock per resource · I²C/SPI/SDMMC are exactly these — priority inversion is not theoretical
CRITICAL-SECTION MATRIX — max CS per task per resource
Task
R1
R2
R3
R4
R5
T
τ_B
—
1
—
1
1
8
τ_C
2
—
1
2
1
10
τ_D
—
4
2
3
—
18
τ_A
6
1
—
—
4
40
Read: τ_A holds R1 for 6 — longest. This drives PCP blocking for everyone else.
RESULT — B_i per protocol
Task
B_PIP
B_PCP
Saving
τ_B
10
4
2.5×
τ_C
10
6
1.7×
τ_D
6
6
no lower task
τ_A
0
0
no lower task
PCP: B = max over resources (max lower CS). PIP: B = sum over lower tasks (max per task). PCP ≤ PIP always.
WHY THIS MATTERS — INVERSION ON THE WIRE
Without a protocol: low-priority τ_A locks R1 (6 units), medium τ_D/τ_C spin, high τ_B starves — unbounded priority inversion.
• PIP: holder inherits blocked task’s priority → τ_A briefly becomes b-priority (2). But chained blocking sums: B_B = 2+4+4 = 10.
• PCP: ceiling per resource = highest priority that ever uses it. Lock only if priority > all ceilings of locked resources. At most one block: B_B = max(4,3,4)=4.
• Result: PCP halves blocking (10→4, 10→6). τ_D ties because only τ_A can block it — single lower task, sum=max.
• Player mapping: R1/R2… are not abstract — I²C bus (AHT20/BMP280 + 2 LCDs), SPI (ST7565R + font ROM), SDMMC (FATFS). Firmware uses Wire.setTimeout(50 ms) + distinct tasks per bus to bound the same effect.
With PIP/PCP, RTA + B: R_i = C_i + B_i + Σ ceil(R_i/T_h)·C_h — re-check slides 3–4 adding B_i.
τ_B with B_PCP=4 → R=2+4=6 ≤8 still OK; but τ_A’s B=0 — the miss was CPU, not lock. Blocking adds nuance, not the root cause here.
06 / 07

## Slide 7
06 — EDF & COMPLEXITY
When RM needs a verdict, EDF needs a proof — and that proof can be exponential or clever
Q5/Q6 from the workbook · bonus/rta/q5_edf_test.py + q6_pdc_complexity.py
Q5 — EDF: PROCESSOR DEMAND CRITERION (Baruah et al. 1990)
τ1 3/10 τ2 15/50/200 τ3 17/100/120 τ4 200/1000/2000
U = Σ C/T
0.617 ≤ 1 ✓ necessary
h(L) = Σ floor((L−D_i)/T_i+1)·C_i
h(L) ≤ L ∀ L
Need & sufficient: check at every deadline point L = k·T_i + D_i up to H. Solver did 600 points up to H = lcm(10,200,120,2000)=6000 — all pass: schedulable under EDF.
L
h(L)
L−h(L)
Verdict
10
3
7
✓
100
35
65
✓
1000
235
765
✓
6000
~3680
~2320
✓
… plus 596 more points — all satisfied. See q5_edf_test.py
Q6 — THE CATCH: H EXPLODES
Naïve: 600 points to H=6000
H grows exponentially (primes!).
Smart: busy period L* = 10
Only 1 point → 600× fewer.
Iteration: L⁰=ΣC → Lᵏ⁺¹=h(Lᵏ). Pseudo-polynomial O(n·D_max/C_min) — polynomial in values, not bit-length.
WHAT WE’D TELL VOGONS — TAKEAWAYS FOR THE PLAYER
Partition wins
Core 0 = Audio (3) + Input (2) • Core 1 = UI/LED/Matrix/Serial/Vogon (1). Two uniprocessors > one overloaded one. RTA per core is what matters.
Prio = policy
Audio prio 3 is our PCP in practice — I²S cannot wait. Input prio 2 avoids SD-open starvation. Rest 1 = best-effort. Matches RM intuition without being RM.
Bound → RTA → PDC
Course flow: sufficient (U≤bound) → exact (RTA+R_B) → EDF (PDC). Our deck walks that ladder with real numbers.
Complexity is real
H=6000 → 600 checks; L*=10 → 1 check. On ESP32, analysis must be offline — runtime can’t afford exponential.
Don’t hand-wave stacks
16K Audio/Input came from real canary trips (_dtoa_r). Schedulability ≠ schedulable + stack overflow.
Repro: bonus/rta/*.py • rebuild: bonus/rta/lenv/bin/python generate_presentation.py
So long, and thanks for all the fish.
07 / 07